## Slide 1
Development of Floor Level Material Transfer Mobile Robot
Project Members
Lalithesh K (RA2211038010007)
Tejas M K (RA2211038010012)
Preetham M (RA2211038010046)
Under the Guidance of
Dr. R. Senthilnathan M.E., Ph.D.
Batch No. MRP02

## Slide 2
21MHP401L/403L - Major Project
Project Objective
The primary objective is to develop an autonomous indoor delivery robot capable of transporting materials between designated locations (Entrances of various rooms) within a single floor of a building (Hi-tech 2nd Floor).
The various tasks to accomplish the objective are:
  To implement mapping and localization using onboard sensors, enabling the robot to autonomously navigate and plan optimal paths within its environment.
  To enable safe and reliable navigation and path planning, ensuring the robot can operate in dynamic environments and maintain a safe coexistence with human activity.
  To develop a user-friendly interface for assigning pickup and drop-off tasks, providing intuitive interaction and real-time status monitoring.
The secondary objectives are:
  To integrate an autonomous docking mechanism that allows the robot to return to a charging station and recharge automatically when the battery level is low.
  To design and implement a developer dashboard that provides remote monitoring, manual pilot control, and system diagnostics for maintenance and performance evaluation.

## Slide 3
Override delivery tasks if charge low
High Level System Block Diagram
Map
Pickup & Dropoff
User Interface
Mission/Task Manager
Mapping & Localisation Module
Global Planner
Perception Module
Obstacle Detection Module
Local Planner
Control Module
Charge Monitoring and Docking
Alerts & Notification System
Dynamic Obstacle in Path
Arrival for Pickup or Dropoff

## Slide 4
Hardware Block Diagram
USB
UART
Digital
PWM
Analog
Mechanical Coupling
Sensor
Power System
Actuation System
Communication System
5V
12V
Motor Encoders
Wi-Fi Module
Direction
Speed
Motor
Motor Driver
Proximity Detection
ZED Mini Stereo Camera
LIDAR
Ultrasonic Sensor
Jetson Nano
Cliff Detection
Primary Perception
Charging Module
Battery
Power Distribution Board
Charging
Discharge State
Charge State
DC to AC Converter
Adapter
IMU (Inbuilt with ZED Camera)
Slip Compensation

## Slide 5
21MHP401L/403L - Major Project
Methodology
System Architecture and Environment Setup
Structural Modifications and Charging Equipment
Mapping and Localization
Navigation and Task Handling
User Interface Development & Integration
Testing and Validation

## Slide 6
Components procured with Price details
S.No | Component Name | Specification | Price /piece (INR) | Quantity required | Total Cost (INR)
1 | Tanna Techbizz Eagle 101 | 4GB |  | 1 | 
2 | Ultrasonic Sensor | HC-SR04 |  | 2 | 
3 | Single-Point 2d LIDAR | Tfmini-Plus |  | 1 | 
4 | LiPO Battery | 10000mah | 5,115.30 | 1 | 
5 | Zed Mini |  |  | 1 | 
6 | DC to AC Inverter |  |  | 1 | 
7 | Optoisolator | 5V – 4 Channel | 67.7 | 3 | 
8 | Logic Level Shifter | 8 Channel |  | 2 | 
9 | Electrical Connectors |  |  |  | 
10 | Carbon Fiber Tubes |  |  | 4 | 
11 | 3D Printing Filament |  |  |  | 

## Slide 7
Progress after zeroth review
Map Creation-Hitech second floor 2D-Map:
CHALLENGE:
1)Traversible area resolution is too low
2) low spatial detail
3) poor navigation accuracy
4) Impact on Localization:Particle filter must search huge state space, Slower convergence, Higher chance of false localization

## Slide 8
SOLUTION:
Splitting single large map to seperates tiles:
Higher Effective Resolution:
more pixels per meter
Corridors appear thicker and clearer
2) Better localization & navigation accuracy:
AMCL particles are constrained
Faster convergence
Lower ambiguity
3) Efficient Costmap & Planning

## Slide 9
CONVERTING THE TILES TO PNG AND PGM+YAML FORMAT:
TILE 1
TILE 2
TILE 3
TILE 4
TILE 5

## Slide 10
2) Map Switching Logic Development:
1)Map Server publishes the active occupancy grid (/map)
2)AMCL localizes the robot within the active map
3)Nav2 plans paths using the current map and localization
4)A custom Tile Switcher node:
  Monitors robot motion
  Detects boundary crossing
  Commands map server to load the next tile
  Resets localization safely

## Slide 11
Map Switching Sequence
1)Robot navigates using Tile 1
2)Tile Switcher monitors odometry
3)Boundary condition is detected
4)Map Server loads Tile 2
5)AMCL is reinitialized with a known pose
6)Nav2 resumes planning

## Slide 13
Aruco Marker Based Localisation
CHALLENGE:
1)Traversible area resolution is too low
2) low spatial detail
3) poor navigation accuracy
4) Impact on Localization:Particle filter must search huge state space, Slower convergence, Higher chance of false localization

## Slide 14: Work split up among the members (in accordance with the work progress after the zeroth review)
Member | Tasks
Lalithesh K | Map Creation, Map Splitting, Map Switching
Tejas M K | Aruco Localisation, Aruco Evaluation, PCB Layout, Jetson Setup
Preetham M | CAD, Fabrication, Circuit Schematic

## Slide 15
Thank You